## Slide 1: Groundwater and surface-subsurface exchange
1
NOTE: Slides for each module are numbered for easier cross-referencing with class notes
NOTE: My slides have TONS of animations and building graphics. These do not translate well to D2L, so it is best to download the power point to work through the logic behind the animations

## Slide 2: Water balance: internal balances
Watershed
Runoff
Streams and lakes
Groundwater
Stream flow generation
Percolation
Soil water
Precipitation
Interception
Snowpack
Surface detention
Throughfall
Snowmelt
Overland flow
Infiltration
Evapotranspiration
Evaporation
Sublimation
Evaporation
Transpiration
Evaporation
Energy
(latent heat)
Energy
2

## Slide 3: Water balance: internal balances
Watershed
Runoff
Streams and lakes
Groundwater
Surface-subsurface exchange
Percolation
Soil water
Precipitation
Interception
Snowpack
Surface detention
Throughfall
Snowmelt
Overland flow
Infiltration
Evapotranspiration
Evaporation
Sublimation
Evaporation
Transpiration
Evaporation
Energy
(latent heat)
Energy
3

## Slide 4: Groundwater: topics covered
Storage in aquifers: describing the amount of water that can be stored in porous media relative to a given change in the total hydraulic head
Water in porous substrate: the fundamental vocabulary and concepts necessary for defining aquifers
Groundwater movement: basic principles of predicting the direction and flux of groundwater movement
Understanding variation in groundwater flow nets: the characteristics of surface and subsurface topography that cause equipotential and flow lines to “bend”
Exchange with surface waters: interpreting the consequences of the intersection of subsurface flow nets with surface waters
Groundwater flux and velocity: basic calculations of different characteristics of groundwater movement based on Darcy’s law
4

## Slide 5: Groundwater: topics covered
Storage in aquifers: describing the amount of water that can be stored in porous media relative to a given change in the total hydraulic head
Water in porous substrate: the fundamental vocabulary and concepts necessary for defining aquifers
Groundwater movement: basic principles of predicting the direction and flux of groundwater movement
Understanding variation in groundwater flow nets: the characteristics of surface and subsurface topography that cause equipotential and flow lines to “bend”
Exchange with surface waters: interpreting the consequences of the intersection of subsurface flow nets with surface waters
Groundwater flux and velocity: basic calculations of different characteristics of groundwater movement based on Darcy’s law
5

## Slide 6: Water in porous media: the basics
Soil (solid) particles
Liquid water
Pore volume
Total volume is sum of
solid, water, and air volumes
Dimensionless ratios [1]
Porosity
Water content (volumetric)
6
*if water is the only liquid in pores

## Slide 7
Water in porous media: pressure head
Hydraulic gradient – change in hydraulic head per unit length of flow path
Hydraulic head – potential mechanical energy of water per unit weight
Elevation head () – potential mechanical energy due to gravity
Pressure head () – potential mechanical energy due to compression/tension
pressure
weight density
Total hydraulic head (hydrostatic):
(gravitational head)
(+)
(-)
7

## Slide 8: Physics of water
8
What is the pressure head at the surface?
What is the pressure head near the bottom?
Why isn’t the water churning due to the difference in pressure?
For a hydrostatic situation (i.e. water not moving) the increase in pressure head with depth is exactly the same as the decrease in elevation head.
~1 atm absolute pressure
0 atm gauge pressure
Total hydraulic head is uniform throughout the bucket
Notes: Before we an start describing the unique physical properties of water, we have to establish some basic context for how we think about reality.
We can build from the basics starting with the most fundamental physical properties. Physical properties are broken down into a couple basic categories: Mass-energy and Space-time. Let’s start as simple as we can get, and just think about liquid water in a bucket.
Q: Water can be described as matter. Based on the definition of matter, what are the 2 properties we know the water in this bucket must have?
A: Water has mass and occupies a volume in space.
Mass and volume are things we can measure. Mass is measured as proportional to the gravitational force of the Earth on the water. This force is also known as the water’s weight. Volume can be measured in many ways.
So if we want to be able to talk to each other about how much mass or how much volume is associated with a given amount of water, then we have to make sure we are thinking in the same context. This is where we have to be sure we are thinking in the same reference frame, and properly defining the dimensions for mass and volume variables in that reference frame. This idea is the domain of dimensional analysis.

## Slide 9: Groundwater: the water table
Subsurface
(gauge pressure)
Saturated
9
Where is the saturated surface?

## Slide 10: Snowmelt: periods and phases
Accumulation and warming phase
T < 0 °C
Ripening phase
T = 0 °C (isothermal)
Snow (ice) particles
Liquid water
Output phase
T = 0 °C (isothermal)
10

## Slide 11: Groundwater: the water table
Subsurface
(gauge pressure)
Saturated
Capillary fringe:
saturated but
Well
Well casing
Screening
Where will the water level be in the well?
Aquifer
(air entry pressure head)
11
Where is the saturated surface?

## Slide 12: Groundwater: aquifers have many scales
Public domain (USGS)
Ogallala aquifer – 450,000 km2
Nyack floodplain aquifer – 16 km2
12

## Slide 13: Groundwater: topics covered
Storage in aquifers: describing the amount of water that can be stored in porous media relative to a given change in the total hydraulic head
Water in porous substrate: the fundamental vocabulary and concepts necessary for defining aquifers
Groundwater movement: basic principles of predicting the direction and flux of groundwater movement
Understanding variation in groundwater flow nets: the characteristics of surface and subsurface topography that cause equipotential and flow lines to “bend”
Exchange with surface waters: interpreting the consequences of the intersection of subsurface flow nets with surface waters
Groundwater flux and velocity: basic calculations of different characteristics of groundwater movement based on Darcy’s law
13

## Slide 14: Groundwater: unconfined aquifer
Subsurface
Saturated
Well
Air pressure =
atmospheric pressure
Storativity or Storage coefficient ()
Unconfined aquifer:
Confining layer - Aquitard
is change in depth of water table for unconfined aquifer
or specific yield
For a given change in head (), the change in volume of water in the aquifer () normalized to the plan area of the aquifer ().
(gauge pressure)
14
Amount of water substrate can hold against gravity.

## Slide 15: Groundwater: confined aquifer
Subsurface
Confining layer - Aquitard
Confining layer - Aquitard
Storativity or Storage coefficient ()
is change in pressure in the aquifer and does not drain pore space
, or specific storage () times the thickness of aquifer ()
15
or specific storage is the change in water content of saturated sediment per change in pressure head, [L-1]
Potentiometric surface

## Slide 16: Groundwater: specific storage vs. specific yield
is change in pressure in the aquifer and does not drain pore space
is change in depth of water table for aquifer and does drain pore space
<<
Volume of water provided by specific storage
Volume of water provided by specific yield
Specific storage
Specific yield
Storativity (or “storage coefficient”)
16
Dominant mechanism of storage in confined aquifers
Dominant mechanism of storage in unconfined aquifers

## Slide 17: Groundwater: topics covered
Storage in aquifers: describing the amount of water that can be stored in porous media relative to a given change in the total hydraulic head
Water in porous substrate: the fundamental vocabulary and concepts necessary for defining aquifers
Groundwater movement: basic principles of predicting the direction and flux of groundwater movement
Understanding variation in groundwater flow nets: the characteristics of surface and subsurface topography that cause equipotential and flow lines to “bend”
Exchange with surface waters: interpreting the consequences of the intersection of subsurface flow nets with surface waters
Groundwater flux and velocity: basic calculations of different characteristics of groundwater movement based on Darcy’s law
17

## Slide 18
Groundwater movement: Darcy’s law
Hydraulic conductivity () – a property of a system of fluid flow that quantifies the ease of fluid movement
Positive water flux is proportional to a
negative hydraulic gradient (for laminar flow through pores)
Henry Darcy
French Engineer
mid-1800s
[L T-1]
[1]
(Darcian flux)
[L T-1]
18
Hydraulic conductivity is strongly controlled by the size and connectivity of pores (and viscosity of the fluid)
This is permeability (not porosity)

## Slide 19
Watershed delineation: consequences of elevation head
Gauging station (pour point)
Flow lines + Equipotential lines =
Flow net
19

## Slide 20: Groundwater: water movement
Subsurface
Saturated
Well
Confining layer - Aquitard
(gauge pressure)
Perpendicular
Horizontal flows: Increase in pressure head with depth is the same as the decrease in elevation head.
Flow line
Equipotential line
20

## Slide 21: Groundwater: flow nets
Subsurface
Saturated
Well
Confining layer - Aquitard
(gauge pressure)
Perpendicular
Flow line
Equipotential line
Equipotential lines are perpendicular to no-flow boundaries
21

## Slide 22: Groundwater: topics covered
Storage in aquifers: describing the amount of water that can be stored in porous media relative to a given change in the total hydraulic head
Water in porous substrate: the fundamental vocabulary and concepts necessary for defining aquifers
Groundwater movement: basic principles of predicting the direction and flux of groundwater movement
Understanding variation in groundwater flow nets: the characteristics of surface and subsurface topography that cause equipotential and flow lines to “bend”
Exchange with surface waters: interpreting the consequences of the intersection of subsurface flow nets with surface waters
Groundwater flux and velocity: basic calculations of different characteristics of groundwater movement based on Darcy’s law
22

## Slide 23: Groundwater: movement through an aquifer
Nyack floodplain aquifer – 16 km2
23
Downstream
Upstream

## Slide 24: Groundwater: flow nets
Upstream
Downstream
Bedrock
Middle Flathead River loses and regains about 30% of the channel flow at low flow conditions on the Nyack floodplain
24
Subsurface topography “bends”
Flow lines
Sediment
Downwelling
Discharge
Upwelling
Recharge

## Slide 25: Groundwater: nested flow paths
25

## Slide 26: Groundwater: nested flow paths
Local flow path
Regional flow path
Intermediate flow path
Recharge
Discharge
Recharge
Discharge
26
József Tóth (1963) A theoretical analysis of groundwater flow in small drainage basins
Surface topography “bends”
Flow lines

## Slide 27: Water balance: conservation in a control volume
Regional groundwater flow direction
Topographic slope direction
Regional groundwater flow
Local groundwater flow
Local groundwater flow
27
for the topographic
watershed on the right

## Slide 28: Groundwater: conductivity is spatially variable
Recharge
Discharge
Recharge
Recharge
Discharge
Recharge
Discharge
Recharge
Discharge
Discharge
28
Flow lines will converge toward higher conductivity areas,
Flow lines will diverge around lower conductivity areas

## Slide 29: Groundwater: geology matters
Hydraulic gradients tend to be steeper where
the hydraulic conductivity is lower.
Hydraulic gradients tend to be shallower where
the hydraulic conductivity is higher.
29
Lower K
Higher K

## Slide 30: Groundwater: map of potentiometric surface
30

## Slide 31: Groundwater: topics covered
Storage in aquifers: describing the amount of water that can be stored in porous media relative to a given change in the total hydraulic head
Water in porous substrate: the fundamental vocabulary and concepts necessary for defining aquifers
Groundwater movement: basic principles of predicting the direction and flux of groundwater movement
Understanding variation in groundwater flow nets: the characteristics of surface and subsurface topography that cause equipotential and flow lines to “bend”
Exchange with surface waters: interpreting the consequences of the intersection of subsurface flow nets with surface waters
Groundwater flux and velocity: basic calculations of different characteristics of groundwater movement based on Darcy’s law
31

## Slide 32: Stream-subsurface exchange: interaction of flow nets and rivers
Groundwater discharges to river
River water balance has a net gain
River recharges groundwater
River water balance has a net loss
Equipotential
lines
(water table surface)
Groundwater flow parallel to river
River water balance is neutral
Flow lines
(arrows indicate direction of downward hydraulic gradient)
32
Plan (overhead) views
of groundwater flow
nets and river reaches
River reaches

## Slide 33
Potentiometric surface of the high plains aquifer near Cheyenne Wyoming
Cheyenne
33

## Slide 34
Is this reach of Crow Creek likely generally gaining water from groundwater discharge or losing water to groundwater recharge?
Down gradient
Losing water to groundwater recharge
34

## Slide 35
Is this reach of Lodgepole Creek likely generally gaining water from groundwater discharge or losing water to groundwater recharge?
Neither, likely net neutral
Down gradient
35

## Slide 36
Is this reach of Horse Creek likely generally gaining water from groundwater discharge or losing water to groundwater recharge?
Gaining water from groundwater discharge
Down gradient
36

## Slide 37: Stream-subsurface exchange: channel water balance
Well
Piezometer
Net loss
Net gain
Same potential means same water level in well/piezometer
37

## Slide 38: Stream – subsurface exchange: Stream depletion zones
Floodplain
Well
River
2013 Montana State Legislature passed SB346
A well in a stream depletion zone is limited to a
20 gallon per minute pump rate and a total of
2 acre feet per year
(normally 35 gpm and 10 acre feet)
Stream depletion zone:
An area where hydrogeologic modeling concludes that pumping at 35 gpm would reduce stream flow by 30% within 30 days.
38

## Slide 39: Stream – subsurface exchange: Stream depletion zones
Floodplain
Drawdown curve,
Cone of depression
39
Charles Vernon Theis
1935

## Slide 40
Susa Stonedahl, accessed 28 October 2014
Stream-subsurface exchange: hyporheic flow
40

## Slide 41: Stream-subsurface exchange: consequences
Transient storage
Tailing
Dispersion
Indicated by “spreading” of tracer
Surface processes
Indicated by “tailing” of tracer
May be caused by exchange with subsurface
41

## Slide 42: Stream subsurface exchange: consequences
Sediment
Upstream
Downstream
Bedrock
Downwelling
Upwelling
Middle Flathead River loses and regains about 30% of the channel flow at low flow conditions on the Nyack floodplain
Recharge
Discharge
Turnover: 30% of the stream channel water has been replaced by groundwater over the reach
42

## Slide 43: Groundwater: topics covered
Storage in aquifers: describing the amount of water that can be stored in porous media relative to a given change in the total hydraulic head
Water in porous substrate: the fundamental vocabulary and concepts necessary for defining aquifers
Groundwater movement: basic principles of predicting the direction and flux of groundwater movement
Understanding variation in groundwater flow nets: the characteristics of surface and subsurface topography that cause equipotential and flow lines to “bend”
Exchange with surface waters: interpreting the consequences of the intersection of subsurface flow nets with surface waters
Groundwater flux and velocity: basic calculations of different characteristics of groundwater movement based on Darcy’s law
43

## Slide 44
Groundwater movement: Darcy’s law
Hydraulic conductivity () – a property of a system of fluid flow that quantifies the ease of fluid movement
Positive water flux is proportional to a
negative hydraulic gradient (for laminar flow through pores)
Henry Darcy
French Engineer
mid-1800s
[L T-1]
[1]
(Darcian flux)
[L T-1]
44
Hydraulic conductivity is strongly controlled by the size and connectivity of pores (and viscosity of the fluid)
This is permeability (not porosity)

## Slide 45: Stream flow measurement
Flux – flow normal (perpendicular) to a surface area
Cross-sectional area, [L2]
Average velocity [L T-1]
Stream flow
[L3 T-1]
45
Notes: This is a stream, and as environmental scientists, we are interested in measuring how much water is in this stream.

## Slide 46: Stream – subsurface exchange: velocity in groundwater
For streams:
For groundwater:
Water flows in the whole channel
Water only flows in the pore spaces
Velocity of groundwater, or the velocity of a solute in groundwater
Darcy Flux
46

## Slide 47: Stream – subsurface exchange: velocity in groundwater
Floodplain
100 m
Distance from well to stream () = 100 m
has recently been detected as a contaminated sampling well
How long will it take () the contaminant to reach the stream?
47

## Slide 48: Groundwater: topics covered
Storage in aquifers: describing the amount of water that can be stored in porous media relative to a given change in the total hydraulic head
Water in porous substrate: the fundamental vocabulary and concepts necessary for defining aquifers
Groundwater movement: basic principles of predicting the direction and flux of groundwater movement
Understanding variation in groundwater flow nets: the characteristics of surface and subsurface topography that cause equipotential and flow lines to “bend”
Exchange with surface waters: interpreting the consequences of the intersection of subsurface flow nets with surface waters
Groundwater flux and velocity: basic calculations of different characteristics of groundwater movement based on Darcy’s law
48