## Slide 1: Well Log Interpretation
Subsurface
Well
0’
97’
6”
6”
1.2”
12’
87’
9.8’
20’

## Slide 2: Well Log Interpretation
Well
0’
97’
6”
6”
1.2”
12’
87’
6’
22’
59’
76’
65’
9.8’
*This particular well did not have pump test results. These are from the MSU EPI well 2
Topsoil
Sand - gravel
Sand stone with gravel
Sand stone
Clay
Gravel - Sand stone
20’

## Slide 3: Stream – subsurface exchange: Stream depletion zones
Floodplain
Drawdown curve,
Cone of depression

## Slide 4
Ground-water equation in polar coordinates
Theis analytical solution
Well function
Aquifer parameter
For an aquifer with a given Sy ,Kh, and h0 pumped a rate of Qw, the Theis analytical solution calculates drawdown (h0 – h) as a function of:
Distance from the well, r
Time elapsed since pumping began, t
* See Dingman textbook pages 441-446 for more info
Pumping rate, [L3T-1]
Drawdown, [L]
Well Function spreadsheet calculator uses these equations
Distance from well [L]
Time elapsed since pumping [T]
Total hydraulic head [L]

## Slide 5
Drawdown
Spread
How would a lower K affect the drawdown and spread?
Drawdown would increase and
Spread would decrease because water movement toward the well would be slower

## Slide 6
Drawdown
Spread
How would a higher K affect the drawdown and spread?
Drawdown would decrease and
Spread would increase because water movement toward the well would be faster

## Slide 7
Drawdown
Spread
How would a lower Sy affect the drawdown and spread?
Drawdown would increase and
Spread would increase because a larger volume of aquifer would need to drain to provide stored water

## Slide 8
Drawdown
Spread
How would a higher Sy affect the drawdown and spread?
Drawdown would decrease and
Spread would decrease because a smaller volume of the aquifer would need to be drained to provide stored water