## Slide 1: Types of transducer: digital transducers
Controller
Transducer
Excitation
Signal
Active or Passive?
Passive
Analog or digital?
Digital
Integrated circuit
Ground
12V OR SW12V
Power supply
SDI-12 Data (Serial Data 1200 baud)
SDM CX port

## Slide 2: Types of transducer: digital transducers
Controller
Transducer
Excitation
Signal
Active or Passive?
Passive
Analog or digital?
Digital
Decagon 5TE soil water content probe (with temperature)
SDI-12 Data (Serial Data 1200 baud) (red)
Power supply (white)
Ground (uninsulated)
12V OR SW12V
SDM C1 port

## Slide 3: Transduction of information: digital transducers
Demonstration
Temperature sensor in Decagon 5TE soil water content digital transducer
Checking and changing the SDI-12 address on a digital transducer
Programming a data logger to power and read a digital transducer