## Slide 1: Precipitation
1
NOTE: Slides for each module are numbered for easier cross-referencing with class notes
NOTE: My slides have TONS of animations and building graphics. These do not translate well to D2L, so it is best to download the power point to work through the logic behind the animations

## Slide 2: Annual water balance
Watershed
Runoff
Precipitation
Evapotranspiration
2

## Slide 3: Hydrologic processes
Watershed
Runoff
Streams and lakes
Groundwater
Stream flow generation
Percolation
Soil water
Precipitation
Interception
Snowpack
Surface detention
Throughfall
Snowmelt
Overland flow
Infiltration
Evapotranspiration
Evaporation
Sublimation
Evaporation
Transpiration
Evaporation
Energy
(latent heat)
Understanding the controls on the water budget is inseparable from understanding of the thermal energy budget.
Energy
3

## Slide 4: Precipitation: topics covered
Causes of precipitation: the local and global circulations that generate the uplift necessary to cause meaningful precipitation
Water in the air: the fundamental vocabulary and concepts necessary for characterizing the physics of water in the air
Types of precipitation: the conditions that dictate the physical state of precipitation (e.g. rain vs. snow)
Measurement of precipitation: the basics of measuring precipitation at given location and translating point measurements to estimates of precipitation over watersheds
Interpreting hyetographs: fundamentals of interpreting visualizations of precipitation over time and the typical summary statistics and probabilistic approaches to analyzing hyetographs
Snow hydrology: a brief introduction to understanding water storage in a seasonal snowpack, including consideration of the energy budget as the determinant of timing of snowmelt
4

## Slide 5: Precipitation: topics covered
Causes of precipitation: the local and global circulations that generate the uplift necessary to cause meaningful precipitation
Water in the air: the fundamental vocabulary and concepts necessary for characterizing the physics of water in the air
Types of precipitation: the conditions that dictate the physical state of precipitation (e.g. rain vs. snow)
Measurement of precipitation: the basics of measuring precipitation at given location and translating point measurements to estimates of precipitation over watersheds
Interpreting hyetographs: fundamentals of interpreting visualizations of precipitation over time and the typical summary statistics and probabilistic approaches to analyzing hyetographs
Snow hydrology: a brief introduction to understanding water storage in a seasonal snowpack, including consideration of the energy budget as the determinant of timing of snowmelt
5

## Slide 6: Precipitation: physics of water in air
Vapor pressure (or absolute vapor pressure): partial pressure of water in air [F L-2]
Partial pressure (): the amount of a gas in a mixture of gasses expressed as the force per unit area exerted by that gas [F L-2] example units: kPa (kN m-2), psi, mm Hg
Absolute humidity: concentration or density of water in the air [M L-3] example units: kg m-3
Saturation vapor pressure(): vapor pressure at saturation, or the limit of how much water vapor the air can hold [F L-2]
Function of temperature
6

## Slide 7: Precipitation: saturation of air
Antoine Equation
Empirical equation for saturation vapor pressure () in units of mm Hg based on temperature in units of °C
7

## Slide 8: Precipitation: physics of water in air
Relative humidity (): ratio of measured vapor pressure to saturation vapor pressure [1]
Often given as percent: < 100% means under-saturated, > 100% means over-saturated
Vapor pressure (or absolute vapor pressure): partial pressure of water in air [F L-2]
Partial pressure (): the amount of a gas in a mixture of gasses expressed as the force per unit area exerted by that gas [F L-2] example units: kPa (kN m-2), psi, mm Hg
Absolute humidity: concentration or density of water in the air [M L-3] example units: kg m-3
Saturation vapor pressure (): vapor pressure at saturation, or the limit of how much water vapor the air can hold [F L-2]
Function of temperature
8

## Slide 9: Precipitation: relative humidity
Relative humidity is
~57%
Over-saturated
Under-saturated
Antoine Equation
Empirical equation for saturation vapor pressure () in units of mm Hg based on temperature in units of °C
Relative humidity () is the absolute vapor pressure () divided by the saturation vapor pressure.
9
is 27 °C and absolute vapor pressure is 2 kPa. What is the relative humidity?

## Slide 10: Precipitation: relative humidity
Over-saturated
Under-saturated
Antoine Equation
Empirical equation for saturation vapor pressure () in units of mm Hg based on temperature in units of °C
Relative humidity () is the absolute vapor pressure () divided by the saturation vapor pressure.
10
is 20 °C and relative humidity is 60%. What is the absolute vapor pressure?

## Slide 11: Precipitation: physics of water in air
Dew point: the temperature at which the air will be saturated with water for a given absolute humidity [T]
In other words, the temperature at which water will start to condense
(if condensation nuclei are available)
11
Relative humidity (): ratio of measured vapor pressure to saturation vapor pressure [1]
Often given as percent: < 100% means under-saturated, > 100% means over-saturated
Vapor pressure (or absolute vapor pressure): partial pressure of water in air [F L-2]
Partial pressure (): the amount of a gas in a mixture of gasses expressed as the force per unit area exerted by that gas [F L-2] example units: kPa (kN m-2), psi, mm Hg
Absolute humidity: concentration or density of water in the air [M L-3] example units: kg m-3
Saturation vapor pressure (): vapor pressure at saturation, or the limit of how much water vapor the air can hold [F L-2]
Function of temperature

## Slide 12: Precipitation: dew point
Relative humidity is
~57%
Over-saturated
Under-saturated
Antoine Equation
Empirical equation for saturation vapor pressure () in units of mm Hg based on temperature in units of °C
12
is 27 °C and absolute vapor pressure is 2 kPa. What is the relative humidity?

## Slide 13: Precipitation: dew point
Relative humidity is
~57%
Dew point is
~18 °C
Over-saturated
Under-saturated
Antoine Equation
Empirical equation for saturation vapor pressure () in units of mm Hg based on temperature in units of °C
13
is 27 °C and absolute vapor pressure is 2 kPa. What is the dew point?

## Slide 14: Precipitation: topics covered
Causes of precipitation: the local and global circulations that generate the uplift necessary to cause meaningful precipitation
Water in the air: the fundamental vocabulary and concepts necessary for characterizing the physics of water in the air
Types of precipitation: the conditions that dictate the physical state of precipitation (e.g. rain vs. snow)
Measurement of precipitation: the basics of measuring precipitation at given location and translating point measurements to estimates of precipitation over watersheds
Interpreting hyetographs: fundamentals of interpreting visualizations of precipitation over time and the typical summary statistics and probabilistic approaches to analyzing hyetographs
Snow hydrology: a brief introduction to understanding water storage in a seasonal snowpack, including consideration of the energy budget as the determinant of timing of snowmelt
14

## Slide 15: Precipitation: steps for formation
1. Air must be cooled to dew point
2. Condensation on nuclei
3. Coalescence into drops or ice of sufficient weight to fall
4. An input of more water laden air
Many mechanisms of cooling, but uplift of moist air into lower pressure conditions higher in the atmosphere dominates the causes of precipitation that are meaningful to watershed water balances
Adiabatic cooling: loss of temperature without loss of heat due to lowering of pressure
15

## Slide 16: Uplift: inherently tied to the energy balance
From Trenberth et al. (2009)
16

## Slide 17: Uplift: global circulation
Shortwave
Shortwave
Shortwave
Shortwave
Shortwave
Shortwave
Shortwave
Shortwave
0 °
Maximum
insolation
90 °N
90 °S
N
Minimum
insolation
Minimum
insolation
17

## Slide 18: Uplift: global circulation
0 °
30 °N
30 °S
60 °N
60 °S
Maximum
insolation
90 °N
90 °S
Low pressure (uplift)
High pressure
High pressure
Hadley Cells
Polar Cell
Polar Cell
High pressure
High pressure
Low pressure (uplift)
Low pressure (uplift)
Ferrel Cell
Ferrel Cell
Polar
Front
Polar
Front
N
Minimum
insolation
Minimum
insolation
Surface wind directions
18

## Slide 19: Uplift: global circulation
Hadley Cells
Polar Cell
Polar Cell
Ferrel Cell
Ferrel Cell
Polar
Front
Polar
Front
N
Surface wind directions
19
0 °
30 °N
30 °S
60 °N
60 °S
Maximum
insolation
90 °N
90 °S
Low pressure (uplift)
High pressure
High pressure
High pressure
High pressure
Low pressure (uplift)
Low pressure (uplift)
Minimum
insolation
Minimum
insolation

## Slide 20: Uplift: global circulation
0 °
30 °N
30 °S
60 °N
60 °S
Down (High P)
Up (Low P)
Down (High P)
Up (Low P)
Up (Low P)
20

## Slide 21: Anomalies and teleconnections
El Niño – Southern Oscillation (ENSO)
NOAA Education resources
21

## Slide 22: Uplift: causes
Convergence at the equator
Frontal convergence (or frontal storms, extra-tropical cyclones) along the polar front
Global circulation
Tropical cyclones (hurricanes, non-frontal)
Form from a local low pressure over warm oceans, feedback between evaporation, uplift, and condensation
Larger scale
Convective storms
Form due to heating of land creating local uplift of moist air
Smaller scale
Orographic effect
Horizontal moving air masses hitting topographic relief
Interacts with other uplift mechanisms to enhance effect of storms with elevation
Movement
Varied scales
22

## Slide 23: Precipitation: topics covered
Causes of precipitation: the local and global circulations that generate the uplift necessary to cause meaningful precipitation
Water in the air: the fundamental vocabulary and concepts necessary for characterizing the physics of water in the air
Types of precipitation: the conditions that dictate the physical state of precipitation (e.g. rain vs. snow)
Measurement of precipitation: the basics of measuring precipitation at given location and translating point measurements to estimates of precipitation over watersheds
Interpreting hyetographs: fundamentals of interpreting visualizations of precipitation over time and the typical summary statistics and probabilistic approaches to analyzing hyetographs
Snow hydrology: a brief introduction to understanding water storage in a seasonal snowpack, including consideration of the energy budget as the determinant of timing of snowmelt
23

## Slide 24: Precipitation: rain or snow?
Why do we care?
Storage of water (water balance, accumulation of snowpack)
Latent and specific heat (energy balance, will snowpack melt)
24

## Slide 25: Precipitation: rain or snow?
25

## Slide 26: Precipitation: rain or snow?
Lower pressures allow snow and sleet at higher temperatures
Higher relative humidity increases the uncertainty of precipitation type
Wet bulb temperature (a metric of heat + latent heat) is a better predictor of precipitation type
26

## Slide 27: Precipitation: topics covered
Causes of precipitation: the local and global circulations that generate the uplift necessary to cause meaningful precipitation
Water in the air: the fundamental vocabulary and concepts necessary for characterizing the physics of water in the air
Types of precipitation: the conditions that dictate the physical state of precipitation (e.g. rain vs. snow)
Measurement of precipitation: the basics of measuring precipitation at given location and translating point measurements to estimates of precipitation over watersheds
Interpreting hyetographs: fundamentals of interpreting visualizations of precipitation over time and the typical summary statistics and probabilistic approaches to analyzing hyetographs
Snow hydrology: a brief introduction to understanding water storage in a seasonal snowpack, including consideration of the energy budget as the determinant of timing of snowmelt
27

## Slide 28: Precipitation: measurement
SNOTEL – managed by Natural Resources
Conservation Service (NRCS)
Precipitation gauge considerations (is “catch” accurate?)
Size of orifice
Height (snow depth)
Shielding (Alter shield)
Obstructions
State changes
28

## Slide 29: Precipitation: measurement
NRCS web page
SNOTEL – managed by Natural Resources
Conservation Service (NRCS)
Snow measurements
Snow pillow (weight of snow)
Sonic range finder (depth of snow)
Snow density
29

## Slide 30: Precipitation: measurement
NRCS web page
SNOTEL – managed by Natural Resources
Conservation Service (NRCS)
Logging and telemetry
Plumbed to manometer (antifreeze)
Pressure transducers
Radio transceiver
30

## Slide 31: Precipitation: sources of error
Measurement error
Scaling point measurements to estimates over large areas
Dealing with missing data
Characterizing spatial distributions
31

## Slide 32: Precipitation: spatial distribution
Strategies
Weighted averages
Interpolate a surface
Arithmetic average
Kriging (geostatistics)
Thiessen Polygons (nearest neighbor)
Hypsometric method
Weight areas based on a model of the spatial distribution of precipitation as a function of elevation
32

## Slide 33
Thiessen polygons or nearest neighbor
Each pixel in the watershed has the same precipitation as the nearest gauge (by Euclidean distance)

## Slide 34
Thiessen polygons or nearest neighbor
Each pixel in the watershed has the same precipitation as the nearest gauge (by Euclidean distance)

## Slide 35
Thiessen polygons or nearest neighbor
Each pixel in the watershed has the same precipitation as the nearest gauge (by Euclidean distance)

## Slide 36
Thiessen polygons or nearest neighbor
Each pixel in the watershed has the same precipitation as the nearest gauge (by Euclidean distance)

## Slide 37
Each pixel in the watershed has the same precipitation as the nearest gauge (by Euclidean distance)
Thiessen polygons or nearest neighbor

## Slide 38
Hypsometric model
Each pixel in the watershed has the precipitation predicted by a model of precipitation vs. elevation
854 mm
708 mm
450 mm
Closest
gauge
Gauge with similar elevation
~580 mm

## Slide 39
Hypsometric method (or average weighted by elevation)
Sample spreadsheet

## Slide 40: Precipitation: topics covered
Causes of precipitation: the local and global circulations that generate the uplift necessary to cause meaningful precipitation
Water in the air: the fundamental vocabulary and concepts necessary for characterizing the physics of water in the air
Types of precipitation: the conditions that dictate the physical state of precipitation (e.g. rain vs. snow)
Measurement of precipitation: the basics of measuring precipitation at given location and translating point measurements to estimates of precipitation over watersheds
Interpreting hyetographs: fundamentals of interpreting visualizations of precipitation over time and the typical summary statistics and probabilistic approaches to analyzing hyetographs
Snow hydrology: a brief introduction to understanding water storage in a seasonal snowpack, including consideration of the energy budget as the determinant of timing of snowmelt
40

## Slide 41: Precipitation: examples of hyetographs and orographic effect
41

## Slide 42: Precipitation: the hyetograph
Elevation = 6860 ft
Elevation = 8100 ft
42
Bar graphs are more appropriate to avoid integration errors
Bar graphs help visualize the timing of precipitation events

## Slide 43: Precipitation: the hyetograph (cumulative)
Elevation = 6860 ft
Elevation = 8100 ft
Annual total volume
43
Cumulative hyetographs are generally easier to compare across gauges and allow immediate visualization of total volumes
Less precipitation
More precipitation

## Slide 44: Precipitation: risk and probabilistic analysis
For hydrograph: flood frequency analysis
Exceedance probability of annual maximum flow
Exceedance probability of annual maximum instantaneous flow
For hyetograph: depth (or intensity) duration frequency analysis
50 year return interval for annual maximum flow is 2000 m3 sec-1
Exceedance probability of annual maximum <duration of interest> rainfall
Exceedance probability of annual maximum 2-hour rainfall
Storm duration
44

## Slide 45: Precipitation: risk and probabilistic analysis
Exceedance probability of annual maximum 2-hour rainfall
13:00
13:30
14:00
14:30
15:00
15:30
16:00
16:30
Depth 2
Depth 1
This is not generally how the calculations are done for precipitation because it may not capture the highest precipitation rate over a given duration.
A “sliding window” summary statistic is used instead.
17:00
45

## Slide 46: Precipitation: risk and probabilistic analysis
Exceedance probability of annual maximum 2-hour rainfall
13:00
13:30
14:00
14:30
15:00
15:30
16:00
16:30
Depth 1
Depth 2
Depth 3
Depth 4
Depth duration
frequency analysis
Intensity duration
frequency analysis
Sliding window
17:00
46

## Slide 47
Figure 4.46 in Physical Hydrology 3rd Edition by Dingman
47

## Slide 48
Figure 4.46 in Physical Hydrology 3rd Edition by Dingman
48

## Slide 49: Precipitation: topics covered
Causes of precipitation: the local and global circulations that generate the uplift necessary to cause meaningful precipitation
Water in the air: the fundamental vocabulary and concepts necessary for characterizing the physics of water in the air
Types of precipitation: the conditions that dictate the physical state of precipitation (e.g. rain vs. snow)
Measurement of precipitation: the basics of measuring precipitation at given location and translating point measurements to estimates of precipitation over watersheds
Interpreting hyetographs: fundamentals of interpreting visualizations of precipitation over time and the typical summary statistics and probabilistic approaches to analyzing hyetographs
Snow hydrology: a brief introduction to understanding water storage in a seasonal snowpack, including consideration of the energy budget as the determinant of timing of snowmelt
49

## Slide 50: Precipitation: rain vs. snow
Elevation = 6860 ft
Elevation = 8100 ft
50

## Slide 51: Precipitation: storage in snowpack
Elevation = 6860 ft
Elevation = 8100 ft
51

## Slide 52: Snowmelt
Elevation = 6860 ft
Elevation = 8100 ft
52

## Slide 53: Snowmelt: water and heat budget
SWE
Temperature and specific heat
P
Precipitation
M
Snowmelt
Evaporation/
Sublimation/
Condensation
E
Latent
LE
Ablation = Total loss =
Snowmelt + evaporation/sublimation
PH
Heat in
Precipitation
MH
Heat in
Snowmelt
Sensible
air
HA
Sensible
ground
HG
K
Shortwave
Radiation
(insolation)
KR
Reflected
shortwave
radiation
Albedo =
Potential to reflect radiation
Net
Longwave
L
Atmosphere
Earth
53
Advection

## Slide 54: Thought exercise: conditions for large melt events
Warm, sunny days
Shortwave radiation
Sensible and net longwave input from warm air
Rain on snow
Precipitation brings in heat and mobilizes water
Condensation (latent heat of vaporization)
Condensation (latent heat of fusion)
What mechanisms of heat exchange are important to snowmelt on...?
54

## Slide 55: Snowmelt: periods and phases
Accumulation period
Temperature < 0 °C and multiday average change in temperature <= 0 C°
Melt period
Warming phase: temperature < 0 °C and multiday average change in temperature > 0 C° (sensible, specific heat of ice)
Ripening phase: temperature = 0 °C (isothermal), added heat melts water,
melt water retained by surface tension (latent heat of fusion)
Output phase: temperature = 0 °C (isothermal), added heat melts water,
weight of melt water overcomes surface tension (latent heat of fusion)
55

## Slide 56: Snowmelt: periods and phases
Accumulation and warming phase
T < 0 °C
Ripening phase
T = 0 °C (isothermal)
Snow (ice) particles
Liquid water
Output phase
T = 0 °C (isothermal)
56

## Slide 57: Sample problem: energy necessary to produce meltwater
57
The snow is 60 cm deep and has a water content (SWE) of 20 cm. If the current snow temperature is -3 °C, what is the area-normalized thermal energy needed to start producing melt water?
Step 1: How much heat is necessary to warm the snow to 0 °C ?
Step 2: How much latent heat is necessary to melt enough snow for the liquid to start overcoming tension?
Warming phase
Ripening phase

## Slide 58: Warming Phase (Sensible Heat)
Equation 5.18d in Dingman Texbook:
Cold Content, or net energy per area required complete the warming phase (warm the snow to its melting point) [E L-2]
Specific heat of ice, 2102 J kg-1 K-1
[E M-1 Θ-1]
Density of Water, 1000 kg m-3
[M L-3]
Snow Water Equivalent [L]
Average Snowpack Temperature minus Melting Point Temperature [Θ]
Mass of water (as ice) per unit area [M L-2]
Notes: Cold content = amount of energy to get to ripening phase (or to get snow to an isothermal state)
Sensible heat, Q = mC delta T (same here but normalized to area so dimensionality is a little different

## Slide 59: Sample problem: energy necessary to produce meltwater
59
The snow is 60 cm deep and has a water content (SWE) of 20 cm. If the current snow temperature is -3 °C, what is the area-normalized thermal energy is needed to start producing melt water?
Step 1: How much heat is necessary to warm the snow to 0 °C?
Step 2: How much heat is necessary to produce enough liquid water to start overcoming tension?
Warming phase
Ripening phase

## Slide 60: Ripening Phase (Latent Heat)
Net energy per unit area to complete the ripening phase [E L-2]
(Equation 5.26 in Dingman Texbook}
(Equation 5.23 in Dingman Texbook)
(Equation 5.25 in Dingman Texbook)
Liquid Water Holding Capacity [L]
Maximum Volumetric Water Content Snow can retain against gravity [L3 L-3]
Latent Heat of Fusion, 0.334 MJ/kg [E M-1]

## Slide 61: Snow Water Equivalent, [L]
melting
hs
hSWE
The amount of water contained in snow, expressed as an area normalized volume
Snow Water Equivalent [L]
Ratio of snow and water density [-]
Snowpack depth [L]
Equation 5.10 in Dingman Texbook:
Notes: Area normalization

## Slide 62: Sample problem: energy necessary to produce meltwater
62
The snow is 60 cm deep and has a water content (SWE) of 20 cm. If the current snow temperature is -3 °C, what is the area-normalized thermal energy is needed to start producing melt water?
Step 1: How much heat is necessary to warm the snow to 0 °C?
Step 2: How much heat is necessary to produce enough liquid water to start overcoming tension?
Warming phase
Ripening phase

## Slide 63: Sample problem: energy necessary to produce meltwater
63
The snow is 60 cm deep and has a water content (SWE) of 20 cm. If the current snow temperature is -3 °C, what is the area-normalized thermal energy is needed to start producing melt water?
Step 1: How much heat is necessary to warm the snow to 0 °C?
Step 2: How much heat is necessary to produce enough liquid water to start overcoming tension?
Not going to give the right units ?!?! Are we wrong?
No, this is an empirical approximation. We are not wrong, but it’s a hint we need to be VERY careful with units.
Warming phase
Ripening phase

## Slide 64: Sample problem: energy necessary to produce meltwater
64
The snow is 60 cm deep and has a water content (SWE) of 20 cm. If the current snow temperature is -3 °C, what is the area-normalized thermal energy is needed to start producing melt water?
Step 1: How much heat is necessary to warm the snow to 0 °C?
Step 2: How much heat is necessary to produce enough liquid water to start overcoming tension?
Step 3: Sum
is necessary for the snowpack to start producing melt water
Warming phase
Ripening phase

## Slide 65: Snowmelt: simple temperature index models
Temperature index approach (empirical)
The mechanisms of heat input all tend to correlate with air temperature
is an empirical linear coefficient
is the temperature of the air
is the melting point temperature
This model tends to work reasonably well, but the value of cannot be independently determined from watershed properties and does not easily transfer between watersheds.
65

## Slide 66: Precipitation: topics covered
Causes of precipitation: the local and global circulations that generate the uplift necessary to cause meaningful precipitation
Water in the air: the fundamental vocabulary and concepts necessary for characterizing the physics of water in the air
Types of precipitation: the conditions that dictate the physical state of precipitation (e.g. rain vs. snow)
Measurement of precipitation: the basics of measuring precipitation at given location and translating point measurements to estimates of precipitation over watersheds
Interpreting hyetographs: fundamentals of interpreting visualizations of precipitation over time and the typical summary statistics and probabilistic approaches to analyzing hyetographs
Snow hydrology: a brief introduction to understanding water storage in a seasonal snowpack, including consideration of the energy budget as the determinant of timing of snowmelt
66