## Slide 1: Water and soils
1
NOTE: Slides for each module are numbered for easier cross-referencing with class notes
NOTE: My slides have TONS of animations and building graphics. These do not translate well to D2L, so it is best to download the power point to work through the logic behind the animations

## Slide 2: Water balance: internal balances
Watershed
Runoff
Streams and lakes
Groundwater
Stream flow generation
Percolation
Soil water
Precipitation
Interception
Snowpack
Surface detention
Throughfall
Snowmelt
Overland flow
Infiltration
Evapotranspiration
Evaporation
Sublimation
Evaporation
Transpiration
Evaporation
Energy
(latent heat)
Understanding the controls of the water balance is inseparable from understanding of the energy balance.
Energy
2

## Slide 3: Soil water: topics covered
Capillarity and negative pressure head: the concepts necessary to quantify the ability of pores to create negative pressure heads that hold water against gravity or move water against gravity
Water in unsaturated porous substrate: extending the fundamental vocabulary and concepts of subsurface waters to cover unsaturated conditions
Soil water flux: extending Darcy’s Law to be able to predict the flux of water through a porous substrate under unsaturated conditions
Predicting infiltration rates: a simpler perspective on predicting infiltration rates based on Green-Ampt theory
Measuring water content: example of the gravimetric technique and an overview of other techniques
Direction of soil water movement: examples of how to calculate total head in unsaturated conditions and infer the direction of hydraulic gradients
3

## Slide 4: Soil water: topics covered
Capillarity and negative pressure head: the concepts necessary to quantify the ability of pores to create negative pressure heads that hold water against gravity or move water against gravity
Water in unsaturated porous substrate: extending the fundamental vocabulary and concepts of subsurface waters to cover unsaturated conditions
Soil water flux: extending Darcy’s Law to be able to predict the flux of water through a porous substrate under unsaturated conditions
Predicting infiltration rates: a simpler perspective on predicting infiltration rates based on Green-Ampt theory
Measuring water content: example of the gravimetric technique and an overview of other techniques
Direction of soil water movement: examples of how to calculate total head in unsaturated conditions and infer the direction of hydraulic gradients
4

## Slide 5: Soil physics: analogy with snow
Accumulation and warming phase
T < 0 °C
Ripening phase
T = 0 °C (isothermal)
Snow (ice) particles
Liquid water
Output phase
T = 0 °C (isothermal)
5

## Slide 6: Soil physics: critical hydraulic thresholds
Soil (solid) particles
Liquid water
Wilting
point
No transpiration
No infiltration by gravity
Yes transpiration
No infiltration by gravity
Field
capacity
Yes transpiration
Yes infiltration by gravity
6

## Slide 7: Water in porous media: the basics
Soil (solid) particles
Liquid water
Pore volume
Total volume is sum of
solid, water, and air volumes
Dimensionless ratios [1]
Porosity
Water content (volumetric)
7
*if water is the only liquid in pores
Saturation

## Slide 8: Soil physics: volumes [L3] of three phases
Soil (solid) particles
Liquid water
Pore volume
Dimensionless ratios [1]
Porosity
Saturation
Density [M L-3]
Water content (volumetric)
Bulk density
(“dry”)
Wet (or total) bulk density
8
*if water is the only liquid in pores

## Slide 9: Soil water: topics covered
Capillarity and negative pressure head: the concepts necessary to quantify the ability of pores to create negative pressure heads that hold water against gravity or move water against gravity
Water in unsaturated porous substrate: extending the fundamental vocabulary and concepts of subsurface waters to cover unsaturated conditions
Soil water flux: extending Darcy’s Law to be able to predict the flux of water through a porous substrate under unsaturated conditions
Predicting infiltration rates: a simpler perspective on predicting infiltration rates based on Green-Ampt theory
Measuring water content: example of the gravimetric technique and an overview of other techniques
Direction of soil water movement: examples of how to calculate total head in unsaturated conditions and infer the direction of hydraulic gradients
9

## Slide 10: Soil water: water content measurement
By weight (in lab):
1. Sample a known soil volume
2. Weigh wet bulk sample
3. Dry sample in oven
4. Weigh dried sample
Intact soil core, = 1500 cm3 = 0.0015 m3
Wet weight (mass)
Dry weight (mass)
Density of solids, = 2800 kg m-3
Density of water, = 1000 kg m-3
Wet bulk density (mass)
Water weight (mass)
Water volume
10

## Slide 11: Soil water: water content measurement
By weight (in lab):
1. Sample a known soil volume
2. Weigh bulk sample
3. Dry sample in oven
4. Weigh dried sample
Density of solids, = 2800 kg m-3
Density of water, = 1000 kg m-3
Water content
11
?

## Slide 12: Soil water: water content measurement
By weight (in lab):
1. Sample a known soil volume
2. Weigh bulk sample
3. Dry sample in oven
4. Weigh dried sample
Neutron probe (in field):
1. Emits “fast” neutrons
2. Return of “slow” neutrons determined by hydrogen atoms
3. Infer water content from hydrogen atoms
Electrical properties (in field):
1. Electrical conductivity or resistivity
2. Electrical permittivity (e.g. measured by Time Domain Reflectometry (TDR))
Emission of radiation (remote sensing):
1. Microwaves
12

## Slide 13: Soil physics: critical hydraulic thresholds
Soil (solid) particles
Liquid water
Wilting
point
No transpiration
No infiltration by gravity
Yes transpiration
No infiltration by gravity
Field
capacity
Yes transpiration
Yes infiltration by gravity
13

## Slide 14: Soil water: topics covered
Capillarity and negative pressure head: the concepts necessary to quantify the ability of pores to create negative pressure heads that hold water against gravity or move water against gravity
Water in unsaturated porous substrate: extending the fundamental vocabulary and concepts of subsurface waters to cover unsaturated conditions
Soil water flux: extending Darcy’s Law to be able to predict the flux of water through a porous substrate under unsaturated conditions
Predicting infiltration rates: a simpler perspective on predicting infiltration rates based on Green-Ampt theory
Measuring water content: example of the gravimetric technique and an overview of other techniques
Direction of soil water movement: examples of how to calculate total head in unsaturated conditions and infer the direction of hydraulic gradients
14

## Slide 15: Soil physics: surface tension and capillarity
Surface tension of water (20 °C) = 73 mN m-1
Surface tension of ethanol = 22 mN m-1
http://web.mit.edu/nnf/education/wettability/gravity.html
15
Hydrogen bonding results in high internal tension

## Slide 16
Source of water (water table) is at bottom of columns
Clay is finer than sand
Sand is coarser than clay
Capillary forces in finer sediments can lift water higher than in coarser sediments
For the same water content, tension tends to be higher in soils with smaller pores
https://youtu.be/Ph-7tQuIbz4?t=292
16

## Slide 17: Soil physics: critical thresholds
porosity > field capacity > wilting point
Figure 7.6 in Dingman text
COARSER
FINER
The ability of soil to hold water against gravity is called capillarity
Capillarity is caused by cohesive and adhesive forces creating tension on water molecules
Capillarity (or tension) increases as sediment/pore size decreases
17
NOT permeability

## Slide 18
Soil physics: revisit hydraulic gradient and head
Hydraulic gradient – change in hydraulic head per unit length of flow path
Hydraulic head – potential mechanical energy of water per unit weight
Elevation head () – potential mechanical energy due to gravity
Pressure head () – potential mechanical energy due to compression/tension
pressure
weight density
Total hydraulic head (hydrostatic):
(gravitational head)
(+)
(-)
(negative pressure head: matric potential, moisture tension, soil water potential, suction head)
18

## Slide 19: Soil water: water potential measurement
Tensiometer:
1. Sealed water-filled chamber with pressure gauge connected to soil by porous cup
2. At equilibrium, pressure in chamber is equal to pressure head in soil
Resistivity block:
1. Block with known vs. relationship (typically gypsum)
2. At equilibrium, pressure head inferred from water content, which is inferred from electrical resistance
19
Gauge
Water filled chamber
Ceramic porous cup

## Slide 20: Soil water: topics covered
Capillarity and negative pressure head: the concepts necessary to quantify the ability of pores to create negative pressure heads that hold water against gravity or move water against gravity
Water in unsaturated porous substrate: extending the fundamental vocabulary and concepts of subsurface waters to cover unsaturated conditions
Soil water flux: extending Darcy’s Law to be able to predict the flux of water through a porous substrate under unsaturated conditions
Predicting infiltration rates: a simpler perspective on predicting infiltration rates based on Green-Ampt theory
Measuring water content: example of the gravimetric technique and an overview of other techniques
Direction of soil water movement: examples of how to calculate total head in unsaturated conditions and infer the direction of hydraulic gradients
20

## Slide 21
Redistribution: direction of water movement
Soil
A
B
20 cm
50 cm
Datum
In what direction does water want to move?
(assuming freshwater)
21
But water may not move if the soil is too dry!
Water wants to move upward because the hydraulic head at depth A (-408 cm) is less than the hydraulic head at depth B (-203 cm).

## Slide 22
Redistribution: direction of water movement
Soil
A
B
20 cm
50 cm
Datum
In what direction does water want to move?
(assuming freshwater)
22
Alternate method using the sign of the hydraulic gradient:

## Slide 23
Redistribution: direction of water movement
Soil
A
B
20 cm
50 cm
Datum
What would the pressure head at A need to prevent water movement?
23
(assuming freshwater)

## Slide 24: Soil water: topics covered
Capillarity and negative pressure head: the concepts necessary to quantify the ability of pores to create negative pressure heads that hold water against gravity or move water against gravity
Water in unsaturated porous substrate: extending the fundamental vocabulary and concepts of subsurface waters to cover unsaturated conditions
Soil water flux: extending Darcy’s Law to be able to predict the flux of water through a porous substrate under unsaturated conditions
Predicting infiltration rates: a simpler perspective on predicting infiltration rates based on Green-Ampt theory
Measuring water content: example of the gravimetric technique and an overview of other techniques
Direction of soil water movement: examples of how to calculate total head in unsaturated conditions and infer the direction of hydraulic gradients
24

## Slide 25
Groundwater movement: Darcy’s law
Hydraulic conductivity () – a property of a system of fluid flow that quantifies the ease of fluid movement
Positive water flux is proportional to a
negative hydraulic gradient (for laminar flow through pores)
Henry Darcy
French Engineer
mid-1800s
[L T-1]
[1]
(Darcian flux)
[L T-1]
25
Hydraulic conductivity is strongly controlled by the size and connectivity of pores (and viscosity of the fluid)
This is permeability (not porosity)

## Slide 26
Soil physics: Darcy’s law in unsaturated conditions
1. Hydraulic conductivity increases with increasing water content ()
Henry Darcy
French Engineer
mid-1800s
26

## Slide 27
Soil physics: Darcy’s law in unsaturated conditions
1. Hydraulic conductivity increases with increasing water content ()
2. Pressure head is negative in unsaturated conditions
Henry Darcy
French Engineer
mid-1800s
27

## Slide 28
Soil physics: Darcy’s law in unsaturated conditions
1. Hydraulic conductivity increases with increasing water content ()
2. Pressure head is negative in unsaturated conditions
3. Pressure head gets more negative with decreasing water content ()
Henry Darcy
French Engineer
mid-1800s
28

## Slide 29
Soil physics: Darcy’s law in unsaturated conditions
1. Hydraulic conductivity increases with increasing water content ()
2. Pressure head is negative in unsaturated conditions
3. Pressure head gets more negative with decreasing water content ()
Henry Darcy
French Engineer
mid-1800s
29

## Slide 30
Soil physics: Darcy’s law in unsaturated conditions
Henry Darcy
French Engineer
mid-1800s
30
1. Hydraulic conductivity increases with increasing water content ()
2. Pressure head is negative in unsaturated conditions
3. Pressure head gets more negative with decreasing water content ()

## Slide 31: Soil physics: application to irrigation
Plant available water
From the National Engineering Handbook, 201-VI
3. Pressure head is a function of water content ()
31

## Slide 32
https://www.youtube.com/watch?v=Ph-7tQuIbz4
32

## Slide 33: Soil physics: infiltration capacity
Horton RE. 1933. The role of infiltration in the hydrologic cycle.
Transactions, American Geophysical Union 14: 446–460.
Infiltration capacity is a critical partitioning mechanism in the watershed, determining how rain water or snow melt is partitioned between:
1. Soil storage and transport
2. Overland flow
What do we need to know about soil to understand mechanisms of infiltration?
1. Characteristics of vs.
2. Characteristics of vs.
33

## Slide 34: Infiltration: controlling pressure head
Not easy to know and :
1. Not easy to control at large scales
2. Not easy to scale to watersheds
Pressure plate
34
How do we calculate and as a function of ?
Rien Van Genuchten
(> 22000 citations)

## Slide 35: Infiltration: Richard’s equation
35
Inputs minus outputs due to change in flux with depth
Lorenzo A. Richards
Soil at
If flux is increasing with depth, then water content must decrease (soil is draining faster than filling)

## Slide 36: Infiltration: Richard’s equation
36
Inputs minus outputs due to change in flux with depth
Lorenzo A. Richards
If flux is decreasing with depth, then water content must increase (soil is filling faster than draining)
Soil at

## Slide 37: Infiltration: Richard’s equation
Two practical problems:
1. Not easy to solve with arbitrary boundary conditions
2. Not easy to know and
Inputs minus outputs due to elevation head
Inputs minus outputs due to pressure head
37
Inputs minus outputs due to change in flux with depth
Lorenzo A. Richards

## Slide 38: Soil water: topics covered
Capillarity and negative pressure head: the concepts necessary to quantify the ability of pores to create negative pressure heads that hold water against gravity or move water against gravity
Water in unsaturated porous substrate: extending the fundamental vocabulary and concepts of subsurface waters to cover unsaturated conditions
Soil water flux: extending Darcy’s Law to be able to predict the flux of water through a porous substrate under unsaturated conditions
Predicting infiltration rates: a simpler perspective on predicting infiltration rates based on Green-Ampt theory
Measuring water content: example of the gravimetric technique and an overview of other techniques
Direction of soil water movement: examples of how to calculate total head in unsaturated conditions and infer the direction of hydraulic gradients
38

## Slide 39
https://www.youtube.com/watch?v=Ph-7tQuIbz4
39

## Slide 40
Nearly saturated, gradient in elevation head (gravitational head) dominates movement
Unsaturated, gradient in pressure head (capillary forces, tension, etc.) dominates movement
Unsaturated, gradient in pressure head (capillary forces, tension, etc.) dominates movement
https://www.youtube.com/watch?v=Ph-7tQuIbz4
40
Infiltration is at its MAXIMUM early
Infiltration is at its MINIMUM late
After ~14 minutes
After ~2 minutes

## Slide 41: Infiltration: wetting fronts and Green-Ampt
Figure 8.20 from Dingman
Increasing water content () [L3 L-3]
0
Increasing depth [L]
Ground surface
[L T-1]
41
When rainfall is
LESS THAN minimum infiltration capacity

## Slide 42: Infiltration: wetting fronts and Green-Ampt
Figure 8.20 from Dingman
Increasing water content () [L3 L-3]
0
Increasing depth [L]
Ground surface
[L T-1]
Infiltration is
limited by
rainfall
42
When rainfall is
LESS THAN minimum infiltration capacity

## Slide 43: Infiltration: wetting fronts and Green-Ampt
Figure 8.21 from Dingman
Increasing water content () [L3 L-3]
0
Increasing depth [L]
Ground surface
Infiltration () is
limited by
saturated hydraulic
conductivity ()
and hydraulic gradient
at the wetting front
Hydraulic gradient
at the wetting front
determined by , or pressure head just below the front
Before “ponding” time (), infiltration is limited by rainfall
43
When rainfall is
GREATER THAN minimum infiltration capacity

## Slide 44: Infiltration: wetting fronts and Green-Ampt
Figure 8.21 from Dingman
Increasing water content () [L3 L-3]
0
Increasing depth [L]
Ground surface
At the time of ponding will be close the surface, and f(t) will be at it’s MAXIMUM
Before “ponding” time (), infiltration is limited by rainfall
44
When rainfall is
GREATER THAN minimum infiltration capacity

## Slide 45: Infiltration: wetting fronts and Green-Ampt
Figure 8.21 from Dingman
Increasing water content () [L3 L-3]
0
Increasing depth [L]
Ground surface
At the time of ponding will be close the surface, and f(t) will be at it’s MAXIMUM
Before “ponding” time (), infiltration is limited by rainfall
45
When rainfall is
GREATER THAN minimum infiltration capacity
After water has infiltrated for a while, will be far from the surface, and f(t) will be its MINIMUM (approaching KS)

## Slide 46: Infiltration: Green – Ampt, when rain > infiltration
is the rate of infiltration [L T-1] at time
is the saturated hydraulic conductivity [L T-1]
is the absolute value of the effective pressure
head at the wetting front [L]
is the difference between initial water content and saturated water content () [1]
is the total cumulative amount of water that has infiltrated up until time [L]
Antecedent conditions matter! (i.e. initial water content)
46

## Slide 47: Infiltration: Green – Ampt, when rain > infiltration
is the rate of infiltration [L T-1] at time
is the total cumulative amount of water that has infiltrated up until time [L]
The effect of decreases over time
and the infiltration rate decreases over time to a minimum value of
The relative effect of pressure gradient decreases over time
The relative effect of gravitational gradient increases over time
47

## Slide 48
Nearly saturated, gradient in elevation head (gravitational head) dominates movement
Unsaturated, gradient in pressure head (capillary forces, tension, etc.) dominates movement
Unsaturated, gradient in pressure head (capillary forces, tension, etc.) dominates movement
https://www.youtube.com/watch?v=Ph-7tQuIbz4
48
Infiltration is at its MAXIMUM early
Infiltration is at its MINIMUM late
After ~14 minutes
After ~2 minutes

## Slide 49
Coarse sediment inhibits flow when pressure head gradient dominates
49
https://youtu.be/Ph-7tQuIbz4?t=914

## Slide 50
Coarse sediment facilitates flow when gravitational head gradient dominates
50
https://youtu.be/Ph-7tQuIbz4?t=914

## Slide 51: Infiltration: Green – Ampt, when rain > infiltration
is calculated from of
is the cumulative effect of
“Implicit” equation, must be solved by iterative technique (trial and error)
51

## Slide 52: Infiltration: Green – Ampt, putting it together
Infiltration excess
Time of ponding
52
Stored in soil

## Slide 53: Soil physics: infiltration capacity
Horton RE. 1933. The role of infiltration in the hydrologic cycle.
Transactions, American Geophysical Union 14: 446–460.
Infiltration capacity is a critical partitioning mechanism in the watershed, determining how rain water or snow melt is partitioned between
1. Soil storage and transport
2. Overland flow
53
Permeability
Antecedent conditions

## Slide 54: Soil physics: macroporosity
Infiltration capacity influences rate of
downward water movement
through macropores
54

## Slide 55: Soil water: topics covered
Capillarity and negative pressure head: the concepts necessary to quantify the ability of pores to create negative pressure heads that hold water against gravity or move water against gravity
Water in unsaturated porous substrate: extending the fundamental vocabulary and concepts of subsurface waters to cover unsaturated conditions
Soil water flux: extending Darcy’s Law to be able to predict the flux of water through a porous substrate under unsaturated conditions
Predicting infiltration rates: a simpler perspective on predicting infiltration rates based on Green-Ampt theory
Measuring water content: example of the gravimetric technique and an overview of other techniques
Direction of soil water movement: examples of how to calculate total head in unsaturated conditions and infer the direction of hydraulic gradients
55