## Slide 1: Stream flow generation
NOTE: Slides for each module are numbered for easier cross-referencing with class notes
NOTE: My slides have TONS of animations and building graphics. These do not translate well to D2L, so it is best to download the power point to work through the logic behind the animations
1

## Slide 2: Stream flow response: Source water separation
Old water
New water
Energy moves faster than water through hydrologic systems.
Mixture of water from different sources
Where did the new water come from?
Where did the old water come from?
2

## Slide 3: Stream flow generation: hillslope hydrology
Bozeman (Sourdough) Creek
3

## Slide 4: Stream flow generation: hillslope hydrology
Runoff = QOUT
Groundwater flow
Precipitation = P
Infiltration /
Recharge
Evaporation (and Transpiration) = EET
4

## Slide 5: Stream flow generation: hillslope hydrology
Runoff = QOUT
Groundwater flow
Precipitation = P
Infiltration /
Recharge
Evaporation (and Transpiration) = EET
5

## Slide 6: Stream flow generation: hillslope hydrology
Precipitation = P
Total interception loss (evaporation)
Interception ()
Net precipitation (throughfall)
Infiltration
Infiltration excess overland flow
Soil water ()
Surface detention ()
6

## Slide 7: Stream flow generation: Infiltration excess
Rising limb
or
hydrograph rise
Falling limb
or
hydrograph recession
Base flow
Peak flow
Delayed flow or Base flow
Quick flow or Event flow
Infiltration excess overland flow = Hortonian overland flow
Foundational concept for decades (including the basis for rational and SCS curve methods)
What if event flow is driven by rainfall rates in excess of soil infiltration capacity?
Robert Elmer Horton
7

## Slide 8: Stream flow generation: Infiltration excess
Old water
New water
Robert Elmer Horton
?
8

## Slide 9: Stream flow generation: hillslope hydrology
Precipitation = P
Total interception loss (evaporation)
Interception ()
Net precipitation (throughfall)
Infiltration
Infiltration excess overland flow
Percolation (recharge)
Groundwater (aquifer) flow
Saturation excess overland flow
Soil water ()
Surface detention ()
Groundwater ()
+ Evapotranspiration
9

## Slide 10: Stream flow generation: Saturation excess
Old water
New water
Saturation excess overland flow = Dunnian overland flow
Led to the current foundational idea known as the Variable Source Area Concept
Saturated areas where groundwater meets the surface must be important to stream flow generation
Thomas Dunne
10

## Slide 11: Stream flow generation: Variable source areas
Variable source area
Ephemeral or intermittent stream
Contours
Streams
11

## Slide 12: Stream flow generation: Variable source areas
12
Capillary
fringe
Water
table

## Slide 13: Stream flow generation: Variable source areas
Hydraulic conductivity (K)
Transmissivity feedback
Kevin Bishop
In many systems, conductivity tends to decrease with depth
13

## Slide 14: Stream flow generation: topographic controls
Variable source area
Ephemeral or intermittent stream
Contours
Streams
Keith Beven
Topography must be important in controlling the extent of variable source areas
“Wetness” is directly related to contributing area and inversely related to the slope
14

## Slide 15: Stream flow generation: topographic controls
Keith Beven
“Wetness” is directly related to contributing area and inversely related to the slope
Topographic Wetness Index
is the contributing area () divided by the contour length (). It is a metric of convergence, or how much water is “funneled” to the location.
A
L
A
L
15

## Slide 16: Stream flow generation: topographic controls
Keith Beven
“Wetness” is directly related to contributing area and inversely related to the slope
A
A
L
L
Topographic Wetness Index
is the contributing area () divided by the contour length (). It is a metric of convergence, or how much water is “funneled” to the location.
16

## Slide 17: Stream flow generation: topographic controls
Keith Beven
“Wetness” is directly related to contributing area and inversely related to the slope
is the local slope (in the steepest direction) of the location. It is a metric of how easy it is for water to leave the location.
a
a
Topographic Wetness Index
17

## Slide 18
Stream flow generation: topographic wetness
18

## Slide 19
Stream flow generation: topographic wetness
Higher
More convergent contributing area,
Lower ,
Higher ,
Wetter
Lower
Less convergent contributing area,
Higher ,
Lower ,
Drier
19

## Slide 20: Contributing area and local slope: The topographic wetness index
From Lin (2006) Vadose Zone Journal 5(1): 317-340
20

## Slide 21: Contributing area and local slope: The topographic wetness index
From Lin (2006) Vadose Zone Journal 5(1): 317-340
The topographic wetness index is a simplification:
When is it more likely to work?
Uniform soil depth in high relief topography
Confining layer below soil more likely to reflect surface topography
When is it less likely to work?
Variable soil depth in low relief topography
Subsurface topography less likely to match surface topography
21

## Slide 22: Stream flow generation: Variable source areas
Variable source area
Ephemeral or intermittent stream
Contours
Streams
22

## Slide 23: Contributing area and local slope: Concepts behind TOPMODEL
Blue is wettest
Green is middling
Yellow is driest
Variable Source Area
23
Stream flow generating area
Non-stream flow generating area

## Slide 24: Stream flow generation: hillslope hydrology
Precipitation = P
Total interception loss (evaporation) + Evapotranspiration
Interception ()
Net precipitation (throughfall)
Infiltration
Infiltration excess overland flow
Interflow (throughflow)
Percolation (recharge)
Return flow
Groundwater (aquifer) flow
Saturation excess overland flow
Soil water ()
Surface detention ()
Groundwater ()
24

## Slide 25: Stream flow generation: interflow
Perched water tables
Local impermeable layer
25

## Slide 26: Stream flow generation: interflow
Hydraulic conductivity (K)
Water will be backed up by the decrease in hydraulic conductivity with depth. This will create hydraulic gradients that will effectively “bend” the flow path to create lateral flow toward the stream
26

## Slide 27: Stream flow generation: measuring interflow
A trenched hillslope for measuring lateral flow in soil
27

## Slide 28: Stream flow generation: macroporosity
28

## Slide 29: Stream flow generation: macroporosity
Jeff McDonnell
Disequilibrium flow in macropores
Infiltration excess
Saturation excess
29

## Slide 30
Diversity in hydrology needs to grow…
Doerthe Tetzlaff
Effi Foufoula-Georgiou
Murugesu Sivapalan
Laura Lautz
Diego Riveros-Iregui
Bridget Scanlon
Mary Hill
Mary Anderson
Ryan Emanuel
30

## Slide 31: Stream flow generation: hillslope hydrology
Precipitation = P
Total interception loss (evaporation) + Evapotranspiration
Interception ()
Net precipitation (throughfall)
Infiltration
Infiltration excess overland flow
Interflow (throughflow)
Percolation (recharge)
Return flow
Saturation excess overland flow
Soil water ()
Surface detention ()
Groundwater ()
Groundwater (aquifer) flow
Groundwater (aquifer) flow
Vertical water movement and storage
Lateral water movement
= Stream flow generation
31

## Slide 32: Stream flow generation: basic controls
(a.k.a. Interflow)
Soil
Surface Permeability
higher
lower
32

## Slide 33: Stream flow generation: source water
Precipitation = P
Total interception loss (evaporation) + Evapotranspiration
Interception ()
Net precipitation (throughfall)
Infiltration
Infiltration excess overland flow
Interflow (throughflow)
Percolation (recharge)
Return flow
Saturation excess overland flow
Soil water ()
Surface detention ()
Groundwater ()
Groundwater (aquifer) flow
Groundwater (aquifer) flow
Vertical water movement and storage
Lateral water movement
= Stream flow generation
33

## Slide 34: Stream flow generation: source water
Discharge
Time
New
Old
+ Evapotranspiration
34

## Slide 35: Stream flow generation: source water
Discharge
Time
Old
Infiltration excess
Precipitation on variable source area
+ Evapotranspiration
35

## Slide 36: Stream flow generation: source water
Discharge
Time
Interflow
Infiltration excess
Precipitation on variable source area
Deep groundwater
Groundwater from variable source area
+ Evapotranspiration
36